## Slide 1
Course: Electronic Engineering UEC001
Topic: Combinational Circuits

## Slide 2: Combinational Circuits
A combinational logic circuit performs an operation assigned logically by a Boolean expression or truth table.
Combinational Circuit is the type of circuit in which output is independent of time and only relies on the input present at that particular instant.
Examples of common combinational logic circuits include: half adders, full adders, multiplexers, demultiplexers, encoders and decoders.

## Slide 3: Design Procedure

## Slide 4: BCD to XS 3 code converter- Design (1)...
      TRUTH TABLE FOR BCD TO XS3 CODE CONVERTER:
Input ( Std BCD code) |  |  |  |  | Output ( XS3 Code) |  |  | 
A | B | C | D | Decimal | w | x | y | z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 2 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 3 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 4 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 5 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 6 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 7 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 8 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 9 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 10 | X | X | X | X
1 | 0 | 1 | 1 | 11 | X | X | X | X
1 | 1 | 0 | 0 | 12 | X | X | X | X
1 | 1 | 0 | 1 | 13 | X | X | X | X
1 | 1 | 1 | 0 | 14 | X | X | X | X
1 | 1 | 1 | 1 | 15 | X | X | X | X

## Slide 5: BCD to XS 3 code converter- Design (2)...
K-maps for simplification and simplified Boolean expressions

## Slide 6: Assignment: Design circuit for BCD to XS 3 code converter-

## Slide 7: Half Adder
A half adder is a type of adder, an electronic circuit that performs the addition of numbers. The half adder is able to add two single binary digits and provide the output plus a carry value.

## Slide 8: Full Adder

## Slide 9: Full Adder
= AB+BC+CA
A full adder is a type of adder, an electronic circuit that performs the addition of numbers. The full adder is able to add three single binary digits and provide the output plus a carry value.

## Slide 10: Full Adder with half adder and OR gate

## Slide 11: Half Subtractor
C
A
B
D
0
0
0
1
0 0 0 0
0 1 1 1
1 0 1 0
1 1 0 0
A
0
B
0
D
0
C
1
0
-1
1
2
1
The half subtractor is also a building block for subtracting two binary numbers. It has two inputs and two outputs. This circuit is used to subtract two single bit binary numbers A and B. The 'diff' and 'borrow' are two output states of the half subtractor.

## Slide 12: Full Subtractor

## Slide 13: 4 Bit Adder

## Slide 14: 4 Bit Adder-cum-Subtractor

## Slide 17: Decoders
A | B | W | X | Y | Z
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Active-high outputs
B
W
X
Y
Z
I0
I1
A
Out0
Out1
Out2
Out3
W = A'.B'
X = A.B'
Y = A'.B
Z = A.B
msb
A decoder is a combinational circuit that converts binary information from n input lines to a maximum of 2^n unique output lines.

## Slide 18: Decoder with Enable
En | A | B | W | X | Y | Z
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | x | x | 0 | 0 | 0 | 0
enabled
disabled
high-level
enable
Enable
B
W
X
Y
Z
I0
I1
A
Out0
Out1
Out2
Out3
En

## Slide 19: Decoder With enable

## Slide 20: Decoders
A | B | W | X | Y | Z
0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0
Active-low outputs
W = (A'.B')'
X = (A.B')'
Y = (A'.B)'
Z = (A.B)'
msb
B
W
X
Y
Z
I0
I1
A
Out0
Out1
Out2
Out3

## Slide 21: Decoders
msb

## Slide 22: Task: Complete truth Table?

## Slide 23: Truth Table

## Slide 24: 4 * 16 decoder constructed with two 3 * 8 decoders

## Slide 25: Combinational Logic Implementation

## Slide 26
z = D1 + D3 + D5 + D7
y = D2 + D3 + D6 + D7
x = D4 + D5 + D6 + D7
ENCODERS
An Encoder is a combinational circuit that performs the reverse operation of Decoder. It has maximum of 2n input lines and ‘n’ output lines. It will produce a binary code equivalent to the input, which is active High. Therefore, the encoder encodes 2n input lines with ‘n’ bits.

## Slide 27
Priority ENCODERS
if there is more than one input at logic level “1” at the same time, the actual output code would only correspond to the input with the highest designated priority. Then this type of digital encoder is known commonly as a Priority Encoder or P-encoder for short.

## Slide 28
2x1 Multiplexer
A Multiplexer is a device that allows one of several analog or digital input signals which are to be selected and transmits the input that is selected into a single medium. Multiplexer is also known as Data Selector. A multiplexer of 2n inputs has n select lines that will be used to select input line to send to the output. Multiplexer is abbreviated as Mux.

## Slide 29: 4x1 Multiplexer

## Slide 32
A 1-line-to-4-line demultiplexer.

## Slide 33: A 1-line-to-8-line demultiplexer.

## Slide 35: Few Examples for practice

## Slide 36: Conversion from Binary code to Gray Code
Let Binary code be b3 b2 b1 b0. Then the respective Gray Code can be obtained is as follows

## Slide 37: FOUR BIT BINARY TO GRAY CODE CONVERTER –DESIGN (1)…
TRUTH TABLE:
MSB
0
+
1
+
1
+
0
+
1
0
1
0
1
1
Binary code
Gray code
INPUT ( BINARY) |  |  |  |  | OUTPUTS (GRAY CODE) |  |  | 
B3 | B2 | B1 | B0 |  | G3 | G2 | G1 | G0
0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 |  | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 |  | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 |  | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 |  | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 |  | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 |  | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 |  | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 |  | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 |  | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 |  | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 |  | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 |  | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 |  | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 |  | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 |  | 1 | 0 | 0 | 0

## Slide 38: FOUR BIT BINARY TO GRAY CODE CONVERTER –DESIGN (2)…
Simplification using K-maps:

## Slide 39
FOUR BIT BINARY TO GRAY CODE CONVERTER –DESIGN (3)
Logic Diagram:

## Slide 40: Gray to Binary
Let Gray Code be g3 g2 g1 g0. Then the respective Binary Code can be obtained as follows:

## Slide 41: FOUR BIT GRAY CODE TO BINARY CONVERTER –DESIGN (1)…
Truth Table:
MSB
1
+
0
+
1
+
0
+
0
1
1
0
0
0
Gray code
Binary code
INPUT ( GRAY CODE) |  |  |  |  | OUTPUTS (BINARY ) |  |  | 
G3 | G2 | G1 | G0 |  | B3 | B2 | B1 | B0
0 | 0 | 0 | 0 |  | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 |  | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 |  | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 |  | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 |  | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 |  | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 |  | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 |  | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 |  | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 |  | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 |  | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 |  | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 |  | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 |  | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 |  | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 |  | 1 | 0 | 1 | 0

## Slide 42: FOUR BIT GRAY CODE TO BINARY CONVERTER –DESIGN (2)…
Simplification using K-Maps:

## Slide 43: FOUR BIT GRAY CODE TO BINARY CONVERTER –DESIGN (3)…
Simplification using K-Maps:

## Slide 44
FOUR BIT GRAY CODE TO BINARY CONVERTER –DESIGN (4)
Logic Diagram: