## Slide 1
Bipolar Junction Transistor (BJT)
Ref. Book: Electronic Devices and Circuit Theory - Robert L. Boylestad and Louis Nashelsky
Notes: 1
1

## Slide 2
Transistors
Invented in 1948 by John Bardeen, Walter Brattain and William Shockley at Bell Lab
Transistors have replaced Vacuum tubes
Transistors offer several advantages
  No heating is required, hence no delays and need less power
  Shock resistant
  Small in size and light in weight
  Require very low operating voltages
  Consume less power and are operationally efficient
  Long life and essentially no aging effect
Notes: 2
2

## Slide 3
Transistor Construction
Bipolar Junction Transistor is a 3-layer semiconductor device consisting of
Either two “n” and one “p” type layers of material – npn Transistor
Or two “p” and one “n” type layers of material - pnp Transistor
First Junction is called Emitter-Base Junction and 2nd junction is called Collector-Base Junction.
Base passes most of these charge carriers (electrons/holes) to collector.
Collector gathers charge carriers from the base.
p
n
n
Transistor has 3 regions: Base (B), Emitter (E), Collector (C)
Emitter emits or injects electrons (for npn) or holes (for pnp) into base.
Width: Width of Emitter & Collector regions is much greater than the base region.
Ratio of the total width to width of the center layer is 150:1. Collector is physically larger than emitter region due too heat dissipation requirements.
Doping:
Emitter is heavily doped.
Base is lightly doped as compared to outer layers (1:10 or less) resulting in less conductivity (more resistance).
Doping of Collector is in between the heavy doping of emitter and light doping of base.
Notes: 3
3

## Slide 4
Transistor - Symbol
Bipolar Junction Transistor: Symbols used for representing npn and pnp transistors are as shown. In npn transistor, emitter has an outward pointing arrowhead.
npn
pnp
In a BJT (Bipolar Junction Transistor) device holes and electrons participate in the injection process into the oppositely polarized material.
All current directions refer to conventional (hole) flow rather than electron flow. Thus arrows in all electronic symbols have a direction defined by this convention.
In pnp transistor emitter has an inward pointing arrowhead.
Therefore, the arrow in the diode symbol is defined by the direction of conduction/ conventional current.
Notes: 4
4

## Slide 5
Transistor Operation
Basic operation of npn and pnp transistors is identical except that the roles played by the electrons and holes are interchanged.
Emitter-Base junction is forward biased
One of the p-n junctions of the transistor is forward biased and the other is reverse biased.
Emitter-Base junction is forward biased, and has a narrow depletion region due to the applied bias, leading to heavy flow of majority carriers from the p - to the n -type material (for pnp transistor).
Base-Collector junction Reverse Biased
Base-Collector junction is connected to power supply as per polarity shown in the diagram (with emitter base junction open):
This is akin to reverse biasing of B-C junction. Thus the flow of majority carriers is zero, resulting in only a minority-carrier flow.
Notes: 5
5

## Slide 6
Transistor Operation
PNP transistor with biasing of both junctions and majority and minority carriers is shown.
Widths of the depletion regions indicates which junction is forward-biased and which one is reverse-biased.
A large number of majority carriers diffuse across the forward biased pn junction into the n -type base.
Since base region is very thin, lightly doped and has low conductivity, very small number of carriers will take high resistance path to the base terminal.  Thus base current is very low and is of the order of µAs, as compared to mAs for the emitter and collector currents.
Most of the majority carriers will diffuse across the reverse-biased junction into the collector region.
In the reverse-biased region these majority carriers appear as injected minority carriers in the n -type base region. Most of the minority carriers in the depletion region will cross the reverse-biased junction.
Notes: 6
6

## Slide 7
Applying Kirchhoff’s current law to the transistor
IE = IC + IB
Transistor Operation
Collector current has two components first component is due to the majority carriers (Ic majority) and the second component is due to the minority carriers (ICO minority).
IC = IC majority + ICO minority
where IC is measured in mA
ICO is measured in µA or nA.
ICO , like reverse current Is for a reverse-biased diode, is temperature sensitive. It can severely affect the stability of a system at high temperature.
Minority-current ICO is called the leakage current and is given the symbol ICO ( Collector current IC with emitter terminal Open).
Notes: 7
7

## Slide 8
As mentioned earlier, Basic operation of npn and pnp transistors is identical except that the roles played by the electrons and holes are interchanged.
Transistor Operation
Here an npn transistors is shown, one of the p-n junctions of the transistor is forward biased and the other is reverse biased.
Emitter-Base junction is forward biased, and has a narrow depletion region due to the applied bias, leading to heavy flow of majority carriers from the n - to the p -type material (for npn transistor).
Collector-Base junction is reverse biased, and has a wide depletion region due to the applied bias.

## Slide 9
Modes of Operations of BJT
Active Mode - Most important mode of operation
- Central to Amplifier operation
- region where the current curves are practically flat
Saturation - Barrier potential of the junctions cancel each other out
causing a virtual short
Cut-Off - Current reduced to zero.
- Ideal transistor behaves like a switch
Reverse Active - Rarely used mode (Inverted Mode of Operation).
Notes: 9
9

## Slide 10
Transistor Configurations
Notes: 10
10

## Slide 11
Transistor Configurations
There are three basic configurations:
  Common Base (CB) Configuration:
    Base terminal is common in input and output circuits.
    Input signal is fed between emitter and base.
    Output is taken between collector and base.
  Common Emitter (CE) Configuration:
    Emitter is common between input and output circuits.
    It acts as an amplifier
  Common Collector (CC) Configuration:
    Collector is common between input and output circuits.
    This is also referred as Emitter follower configuration.
    CC provides high input resistance and low output resistance feature.
Notes: 11
11

## Slide 12
Common Base Configuration
Notes: 12
12

## Slide 13
Common Base Configuration
CB Configuration for “pnp” transistor is shown here.
All the current directions are as defined by the choice of conventional flow i.e. all current directions refer to conventional (hole) flow.
  the direction of IC wrt polarity of VCC
Thus, IE = IC + IB
Applied biasing for pnp transistor establishes current in the direction as indicated for each branch. This is confirmed by following: -
  Direction of IE with respect to (wrt) polarity of VEE and
Notes: 13
13

## Slide 14
Common Base Configuration
CB Configuration for “npn” transistor is shown here.
All the current directions are as defined by the choice of conventional flow i.e. all current directions refer to conventional (hole) flow.
Thus, IE = IC + IB.
Applied biasing for pnp transistor establishes current in the direction as indicated for each branch. This is confirmed by following
  Direction of IE with respect to (wrt) polarity of VEE and
  the direction of IC wrt polarity of VCC .
Notes: 14
14

## Slide 15
Transistor Performance Characteristics
Following two sets of characteristics define the behavior of a transistor : -
IE
VBE
(b) Output Characteristics or Collector Characteristics - defined by the parameters of the output side of the circuit. IC vs VCB
(a) Input or Driving point Characteristics: IE vs VBE
IC
VCB
The input characteristics for the common-base configuration relates an input current (IE) to an input voltage (VBE) for different levels of output voltage (VCB).
Increasing levels of VCB have very small effect on the characteristics that can be ignored.
For fixed values of collector voltage (VCB), the emitter current increases as the base-to-emitter voltage is increased, in a similar manner to that of diode characteristics.
Input/Driving Point Characteristics
Notes: 15

## Slide 16
Equivalent Model for B-to-E Region in dc Mode
For fixed value of collector voltage VCB , input characteristics graph of a transistor resembles the diode characteristics. Since, any change in VCB has a very small effect on the emitter current IE , it is ignored to depict the input characteristic graph at Fig A.
A
B
C
VBE = 0.7 V
Second Approximation is to ignore the slope of the curve i.e. ignore the resistance of the forward-biased junction. The characteristics graph reduces to Fig C.
Piece-wise linear approach results in graph at Fig B as first approximation.
This is used for all dc analysis of transistor networks. This implies that once a transistor is in the “ON” state, the base-to-emitter voltage will be assumed to be VBE = 0.7 V
Notes: 16
16

## Slide 17
Common Base Output/Collector Characteristics
The output characteristics relate output current (IC) to output voltage (VCB ) for different levels of input current (IE ).
VCB
IC
IE
  Active
The output or collector characteristics has three basic regions of interest:
The active region is normally employed for linear (undistorted) amplifiers.
  Saturation
  Cut Off
Notes: 17
17

## Slide 18
Common Base Output/Collector Characteristics
– Active Region
In Active Region, base–emitter junction is forward-biased, and collector–base junction is reverse-biased.
VCB
IC
At the lower end of the active region:
Reverse Saturation current ICO is also referred as ICBO (C-to B current with the emitter leg open). Since ICO is very low, it can be ignored.
(a) Emitter current (IE) is zero, and
(b) Collector current, which is due to the reverse saturation current ICO ,is of the order of μAs as compared to the vertical scale of the graph for IC (mA), so it appears on horizontal axis as IC= 0.
Notes: 18
18

## Slide 19
Collector to Base Voltage VCB has a negligible effect on the collector current IC in the active region leading to a conclusion that IE ≈ IC in the active region.
ICBO , like Is for the diode (both are reverse leakage currents), is temperature sensitive.
Common Base Output/Collector Characteristics – Active Region
VCB
IC
As the emitter current increases above zero, the collector current IC also increases and is generally equal to that of the emitter current IE.
At higher temperatures, the effect of ICBO may become an important factor as it increases rapidly with temperature.
Notes: 19
19

## Slide 20
VCB
IC
Common Base Output/Collector Characteristics –Saturation Region
Saturation region is to the left of VCB = 0 V, in which the base–emitter and collector–base junctions are forward biased.
Forward bias means that collector (for pnp transistor) region is made positive with respect to base (n-type). This causes hole current to flow from p-side across the collector junction to n-side (base).
Collector current IC increases rapidly with slight increase in collector-base Voltage VCB (for pnp transistor). The collector current may increase to become positive if the forward bias is sufficiently large.
VCB = 0 V,
Notes: 20
20

## Slide 21
Common Base Output/Collector Characteristics – Cut-Off Region
In the Cut-off region, the collector current is 0 A.
VCB
IC
Cut-off Region:
It is region of operation where the base–emitter and collector–base junctions of a transistor are both reverse-biased.
Notes: 21
21

## Slide 22
Common Base Output Characteristics - Breakdown Region
As the applied voltage VCB increases, there is a point where the curves take a upswing, which is due to an avalanche effect.
VCB
IC
The largest permissible base-to-collector voltage is labeled as BVCBO or V(BR)CBO. Letter “O” represents that the emitter leg is in the open state.
Reason: Base-to-collector junction is reversed biased in the active region, there is a point where too large a reverse-bias voltage will lead to the avalanche effect.
This results a large increase in current for small increase in the base-to-collector voltage.
Notes: 22
22

## Slide 23
In the DC Mode, the levels of IC and IE are due to the majority carriers, and are related by a quantity called alpha (α), the Common-Base Current Gain
Common Base Current Gain αdc (Alpha)
α for all practical devices typically extends from 0.90 to 0.998. It is also referred as αdc.
Since alpha α is defined solely for the majority carriers, equation
The thinner and more lightly doped is the base , greater is the value of αdc. However, it cannot exceed unity.
So for IE = 0 mA, IC appears to be 0 mA for the different values of VCB.
IC = IC majority + ICO minority
becomes IC = α IE + ICBO
when IE = 0 mA, IC = ICBO , the level of ICBO is so small that it is virtually undetectable on the graph.
For ac situations where the point of operation moves on the characteristic curve, an ac alpha is defined as small change in collector current divided by the corresponding change in IE with the collector-to-base voltage held constant.
Current Gain αac for AC Mode:
αac = ΔIC / ΔIE with VCB being constant
For most situations the magnitudes of αac and αdc are quite close.
Notes: 23
23

## Slide 24
Common Emitter Configuration
Notes: 24
24

## Slide 25
The emitter, collector, and base currents are shown in their actual conventional current direction. Though the transistor is in CE configuration , the currents described for the CB configuration are still applicable. IE = IC + IB and IC = αIE
The common-emitter configuration has the emitter common to both the input and output terminals
Common Emitter (CE) Configuration
Two sets of characteristics necessary to describe the behavior of the common-emitter configuration are :
  Input or base–emitter circuit and
  Output or collector–emitter circuit.
Notes: 25
25

## Slide 26
CE Input Characteristics
The input characteristics are a plot of the input current (IB) vs the input voltage (VBE) for a range of values of output voltage (VCE).
In the Active Region of a Common-Emitter amplifier, the base–emitter junction is forward-biased, whereas the collector–base junction is reverse-biased.
The active region of the common-emitter configuration is used for voltage, current, or power amplification.
Similar conditions exist in the active region of the common-base configuration.
Notes: 26
26

## Slide 27
CE Output Characteristics
Curves of IB are not as horizontal as those obtained for IE in the Common-Base configuration, indicating that the collector-to emitter voltage influences the magnitude of the collector current.
Active region for the CE configuration has the curves for IB that are nearly straight and equally spaced. This region exists to the right of vertical dashed line at VCE sat and above the curve for IB equal to zero. This region is used for for voltage, current, or power amplification.
For the common-emitter configuration the output characteristics are a plot of the output current (IC ) vs output voltage (VCE ) for a range of values of input current (IB).
Magnitude of IB is in μAs as compared to mAs of IC .
The region to the left of VCEsat is called the saturation region.
Notes: 27
27

## Slide 28
Cutoff Region for CE & CB Configuration
The cutoff region for the CE configuration is not as well defined as for CB configuration. The Figure shows that IC ≠ 0 when IB = 0.
For the CB configuration, when the input current IE = 0, the collector current is equal only to the reverse saturation current ICO. So the curve IE = 0 falls on the voltage axis itself.
Notes: 28
28

## Slide 29
Difference in Characteristics of CB and CE Configuration
Reason for difference in collector characteristics of CB & CE configurations is derived here:
Circuit Condition related to ICEO - Collector to Emitter Current with base open
Hence, Collector current defined for the condition
IB = 0 mA is denoted as ICEO for IB = 0 μA
If Base Current is taken as IB = 0 and α = 0.996,
For linear amplification purposes in CE configuration, region below IB = 0 μA should be avoided if an undistorted output signal is required and cut-off for CE configuration is the region defined by IC = ICEO
(IE = IC + IB)
Collector Current
Since, Emitter Current is
If ICBO = 1 μA when IB = 0 , this will yield IC = 250 X 1 μA = 0.25 mA
IC can be rewritten as:-
Notes: 29
29

## Slide 30
In the DC Mode the levels of IC and IB are related by a quantity called beta called Common-Emitter Current Gain
Beta (ᵝdc) – Common-Emitter Current Gain
where IC and IB are determined at a particular operating point on the characteristics. Common-emitter current gain in dc mode is also referred as ᵝdc.
For practical devices the level of ᵝdc typically ranges from about 50 to over 400.
Similar to α, the parameter ᵝdc reveals the relative magnitude of one current with respect to the other. For a device with a ᵝdc of 200, the collector current is 200 times the magnitude of the base current.
Beta (ᵝac)
AC Mode: In CE configuration, collector current is the output current and the base current is the input current. There is an associated amplification factor defined ᵝac for ac situations and is given by
Hence, ᵝac is referred as common-emitter forward-current amplification factor.
Notes: 30
30

## Slide 31
Relationship Between Beta & Alpha
Current Gain of a transistor in CB Config
Beta provides a direct link between current levels of the input
and output circuits for a CE configuration IC = β.IB
and IE = IC + IB
Eq-1 & Eq-2 gives Collector current ICEO = ( β +1). ICBO
ICEO = β . ICBO (ICBO being small)
Collector current when IB = 0 is given by …..Eq-2
Solving above equations yields …...Eq-1
Current Gain of a transistor in CE Config
Refer Slide 23
IE = IC + IB
Solving the equation yields following results:
IE = (β + 1) IB
IE = β IB + IB
Or
Notes: 31
31

## Slide 35
BJT as a Switch

## Slide 36
BJT Biasing
Fixed Biasing
Notes: 36

## Slide 37
BJT Biasing - Fixed Bias Configuration
This is the simplest transistor dc bias configuration. The equations and calculations are applicable to both types of transistors (npn & pnp) merely by changing current directions and voltage polarities.
For analysis, the dc supply VCC can be separated into two supplies to separate input and output circuits. It also reduces the linkage between the two to the base current IB .
The current directions are as shown.
For the dc analysis, the network can be isolated from the indicated ac levels by replacing the capacitors with an open-circuit equivalent, because the reactance of a capacitor is infinity for dc.
Notes: 37

## Slide 38
BJT Biasing - Fixed Bias Configuration
IBRB = VCC - VBE
Forward Bias of Base-Emitter
Consider the base–emitter circuit loop first, the Kirchhoff’s voltage equation in the clockwise direction for the loop gives
+VCC - IBRB - VBE = 0
Supply voltage VCC and the base–emitter voltage VBE are constants, the selection of a base resistor RB sets the level of base current for the operating point.
Notes: 38

## Slide 39
Magnitude of the collector current is related directly to IB through IC = ᵝ IB
BJT Biasing - Fixed Bias Configuration
Collector-Emitter Loop
Collector–emitter section of the network shows the direction of current IC and the resulting polarity across RC .
Value of RC will determine the magnitude of VCE , as worked out by applying Kirchhoff’s voltage law:
VCE = VCC - ICRC
Base Current IB is controlled by RB and Collector Current IC is related to IB by a constant ᵝ.
Magnitude of IC is not a function of the resistance RC . Changing RC to any level will not affect the level of IC in the active region of the device.
Notes: 39

## Slide 40
While in saturation, the collector-to-emitter voltage is at or below VCEsat. Fig-B shows that current is relatively high, and the voltage VCE is assumed to be 0 V. Applying Ohm’s law, resistance between collector and emitter terminals can be determined:
Transistor Saturation
Saturation for a transistor occurs when collector current for a specific design has reached its maximum value. On changing the design, the saturation level may rise or drop. Highest saturation level is a limit provided by the manufacturer.
Fig-A
Fig-B
Fig-C
Fig-D
In an amplifier, saturation state is avoided as the base–collector junction is no longer reverse-biased and the output signal gets distorted. Fig-A and B show the Operating point-Q in the saturation region.
Thus for the fixed-bias configuration of Fig-D , ICsat can be obtained by shorting C & E terminals:
Applying the above result to the network shown in Fig-C, as RCE =0, VCE will also become zero while ICsat will be the current.